# The DPG File Format (Nintendo DS MPEG)
Information summed up by spacy
All values little endian (least significant byte at lowest adress)
Offsets have to be multiples of 4 Bytes (padding)
0x0000: Hexadecimal number
Offset (Versions)	Size	Description
0x0000	4 Bytes	DPG version ID: / DPG0: 0x30475044 / DPG1: 0x31475044 / DPG2: 0x32475044 / DPG3: 0x33475044
0x0004	4 Bytes	Total number of frames
0x0008	4 Bytes	Frames per second * 0x100
0x000C	4 Bytes	Sound frequency (Samplerate) in Hz
0x0010	4 Bytes	Sound channels
0x0014	4 Bytes	Adress of audio stream
0x0018	4 Bytes	Size of audio stream in bytes
0x001C	4 Bytes	Adress of video stream
0x0020	4 Bytes	Size of video stream in bytes
0x0024 (DPG2/3)	4 Bytes	Adress of GOP List
0x0028 (DPG2/3)	4 Bytes	Size of GOP List
0x002C (DPG2/3) / 0x0024 (DPG1)	4 Bytes	Pixel color format

### Annotations
###### Sound channels:
0: Built-in MPEG-1 Audio Layer 2 (MP2) audio stream
1: GSM 1ch
2: GSM 2chs
3: Built-in OGG Vorbis audio stream
###### GOP List:
Holds a list of all GOPs (Group Of Pictures) in the video stream for faster navigation.
Every GOP List entry consists of the following:
4 Byte - Frame Index number at which a MPEG-1 sequence header appears
4 Byte - Offset (address) of this header. Counted from start of video stream, not from DPG file start
###### Pixel color format:
Introduced since DPG2. DPG0 defaulted to RGB24.
0: RGB15 (speed)
1: RGB18 (default)
2: RGB21 (quality)
3: RGB24 (old default)
### Recommended encoder settings for MoonShell v1.71:
###### Audio
audio codec: MPEG-1 Audio Layer 2 (mp2)
- audio sampling frequency: 32000 Hz
- audio bitrate:
  - mono: 64 kbps
  - stereo: 128 kbps
###### Video
- video codec: MPEG-1 Video
- video frame rate: up to 25 frames per second
- video bitrate: up to 448 kbps
- video size of 256x192 (4:3) or 256 x144 (16:9)
Other frequencies, bitrates and OGG Vorbis streams are buggy, do not use them.
If you hear or see skips when the video plays, try to lower the bitrates or the video frame rate.